## Slide 1: Adaptive Navigation of Multi-Robot Systems in Vector Fields
Christopher Waight
Santa Clara University
Mechanical Engineering Department
May 17, 2024
Notes: Kyra rini
Kitts Lee
Marks Neumann

## Slide 2: Agenda
Introduction
Problem Statement
Literature Review
Methodology
Preliminary Results
Expected Outcomes
Timeline
Implication of Findings
Summary
Question and Answers

## Slide 3
Robots, Multirobot systems, and Adaptive Navigation
Scalar Field Features
Scalar Field Primitives
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 4: Introduction
Robotics
Autonomous (Adaptive)
Single Robot Systems
Multi-Robot Systems
Adversarial
Collaborative
Human Controlled
Human in the Loop
Formation Control
Task Execution
Navigation
Scalar Fields
Vector Fields
Autonomous (Conventional)
Independent
Memory Based
Memory Free
Adaptive Navigation is the process of altering a vehicles’ pose and trajectory in response to real time measurements.
Multirobot Systems have advantages over single robot systems including:
Expanded Coverage
Redundancy
Information Sharing
Memoryless adaptive navigation methods are also known as reactive control primitives.
Notes: What is a control primitive?
  Reactive
  Instantaneous
  Proven Results in scalar field MRS Navigation
  Pro: low compute, quick response
  Cons: Vulnerable to noise and local extrema

## Slide 5: Multirobot Scalar Field Adaptive Navigation
Scalar Feature | Application Examples
Maximum | Source of pollution, radiation, gas, emission
Minimum | Quiet/safe spot, anoxic point
Contour | Safety perimeter, service threshold
Ridge / Plume | Path to impact area or optimal service
Trench | Path of max attenuation or min exposure
Saddle Point | Low exposure (energy) path btw max’s (min’s)
Front | Dramatic change that can stimulate activity
Notes: Insert success slides here showing MR AN

## Slide 6: Robot Clusters - Simulations
Extrema Finding Contour Following Ridge/Trench Following
Saddle Point Finding Front Characterization

## Slide 7
Problem Statement
Motivation
Challenges
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 8: Can we design and analyze adaptive navigation methods for multirobot systems to maneuver through complex and dynamic vector fields to specified regions and trajectories interest?

## Slide 9: Can we design and analyze adaptive navigation methods for multirobot systems to maneuver through complex and dynamic vector fields to specified regions and trajectories interest?
Motivation to develop AN in Vector Fields :
  Autonomous Navigation
  Energy Efficiency
  Obstacle Avoidance
  Cross-Sectoral Applications
Challenges:
  Computational Constraints
  Time-Varying Environment
  Imperfect Communication
  Stability
  Robot-Environment Interaction

## Slide 10
Artificial Vector Fields and Natural Vector Fields
Vector Fields via Superposition
Simulation Tools
Indoor Test Beds
Potential Outdoor Test Beds
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 11: Adaptive Navigation in Vector Fields
  Artificial Vector Fields
  Robot systems create artificial vector fields and are used to guide individual robot navigation. [17],[18], [19], [21], [29]
  Natural Vector Fields
  Cooper, Ryan, et al. "Initial Study of Multirobot Adaptive Navigation for Exploring Environmental Vector Fields.” [13]
  Vector Field Modelling
  2x Control Primitives
  Test Bed
Notes: Potential Field == Artificial Vector Fields (work on this explanation) https://medium.com/@rymshasiddiqui/path-planning-using-potential-field-algorithm-a30ad12bdb08

## Slide 12: Vector Fields via Superposition of flows
meters
meters
meters
meters
meters
meters
meters
meters
meters
meters
meters
meters

## Slide 13: Indoor Test Bed
  Omnibots
  RGB Sensor
  Centralized computation
  TCP/IP
  RGB color plots
  OptiTrack provides visual feedback

## Slide 14: Initial Control Primitives
Vector 2 Scalar Technique
zi = || || = magnitude of vector reading for robot (i)
= Velocity of cluster frame
--------------------------------------------------------- =k
Direction Follower Technique
Normalize Compute vector Move Cluster in direction of
-------------------------------------------------------=k
meters
meters

## Slide 15: Open Questions
  Can we design and analyze adaptive navigation methods for multirobot systems to maneuver through complex and dynamic vector fields to specified regions and trajectories interest?
More information? More features?
Stability? Robustness?
Scalability? Shape and performance?
More robots? Imperfect communication between robots?
Discrete sampling?
3D?

## Slide 16
Cluster Space Control Architecture
Control Block Diagram
Simulation Tools
Indoor Test Beds
Potential Outdoor Test Beds
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 17
Cluster Control Architecture
Perfect Communication
Randomized cluster variables
Centralized Control Architectures

## Slide 18: Control Block Diagram

## Slide 19: Simulation
Python 3.9 w/ standard libraries (numpy, matplotlib)
Superpositions of curl free and divergence free components.
Robots are Point masses with first order dynamics
meters
meters
meters
meters

## Slide 20: Test Bed

## Slide 21: Outdoor Tests
Kayaks at Elkhorn Slough

## Slide 22
Areas of Interest Identified
Using Existing Primitive to find Stagnation Point
New Primitive to traverse Separatrix
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 23: Regions of Interest
Region of Interest | How to Model | Importance
Extrema points | Sinks , Sources , Dipoles Rankine Vortex , Fixed Vortex, Free Vortex Sink + Vortex, Source + Vortex, Spring in Stream Opposing Vortices , Corotating Vortices | Location of a spring in a stream Source of magnetic pole Centre of gravity
Equimagnitude Contours | Sinks, Sources , Dipoles Rankine Vortex , Fixed Vortex Free Vortex, Sink + Vortex, Source + Vortex Spring in Stream, Opposing Vortices, Corotating Vortices | Staying within safe operating conditions
Fastest Flow Stream | Corotating Vortices, Superimposed Linear Streams, Spring in Stream Dipole, Vortex in Stream Opposing Vortices, Rankine Vortex | Locate wall of hurricane Fastest Tailwinds Fastest flow for fish or debris
Separatrix | Dipole , Vortex in stream Opposing Vortices, Opposing Streams, Spring in Stream, Corotating Vortices | Path that delineates bifurcating trajectories
Stagnation Point | Spring in Stream, Opposing Vortices Vortex in Stream, Opposing Streams Superimposed Linear Streams | Tracking Heat Waves
Transition Flow | Superposition of flows in sub-areas | Moderate Travel zone

## Slide 24: Navigation to Stagnation Point
meters
meters
Notes: Add in algorithm.

## Slide 25: Stagnation point
Notes: A parabola is the limit curve of a pencil of ellipses with a common vertex and one common focus, as the other focus is moved to infinity to the right, and also the limit curve of a pencil of hyperbolas with a common vertex and one common focus, as the other focus is moved to infinity to the left.
Units, a

## Slide 26: Navigation to Stagnation Point
meters
meters
zi = || || = magnitude of vector reading for robot (i)
= Velocity of cluster frame
=k
4
Notes: Add in algorithm.

## Slide 27: Separatrix Riding Technique
meters
meters

## Slide 28: Separatrix Riding Technique
A separatrix is a boundary in phase space separating regions of different dynamics.
Nonlinear field  Nonlinear control What is the sliding mode? How do I chatter?

## Slide 29: Separatrix Riding Technique
  SUM = Calculate the vector sum
  A = Choose vector with largest cosine similarity to SUM
  B = Choose vector with smallest cosine similarity to A
  =k B
SUM

## Slide 30
Expected Results
Expected Challenges
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 31: Expected Results at Completion
Development of a simple Vector Field modelling tool
Catalog of Vector Field Features
Design and Analysis of Vector Field Primitives
Experimental verification of 2D cases on indoor test bed
Dry run of outdoor experiment
Notes: Stability (within certain bounds or in the sense of Lyapunov).
Performance as a function of robots.
Robustness to noise.
Performance as a function of shape.
Computational Scalability Analysis
Best Use Cases

## Slide 32: Expected Challenges and Mitigations
Imperfect communication  Decentralized controller.
Computation time  BigO Runtime Optimization
Robot Collison  A self collision avoidance
Degenerate Formations  Singularity avoidance techniques
Dynamic Environments  Temporal modelling
3D Visualizations – Unreal Engine?

## Slide 33
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implication of Findings Summary Question and Answers

## Slide 34: Next Steps
2024
May/June – Rebuild Simulation tools and baseline of indoor testing
July/Aug – Stability Analysis of current primitives
Sep/Oct – Performance Analysis with increasing number of robots
Nov/Dec – Indoor Testing
2025
Jan/Feb – Search for new primitives (2D and 3D)
Mar/April – Stability Analysis and Big O analysis
May - Indoor Testing
June/July – Plan, Design, Execute Outdoor Test
Aug / Sep - Decentralized control and discrete sampling Analysis
Oct – Indoor Testing
Nov – Thesis Writing and Defending
Dec – Hand off

## Slide 35
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implications Summary Question and Answers

## Slide 36: Implications of Findings / Potential Next Steps
Autonomous Navigation of Vector Fields.
Efficiencies in navigation and in search.
Incorporation into existing controllers.
Cross sectoral applications and multi-domain use cases:
Finding fastest flow for debris collection
Obstacle avoidance routines
Aerial Drones efficiencies with tailwinds

## Slide 37
Problem Statement
Importance
Recap of Current Efforts
Introduction Problem Statement Literature Review Methodology Preliminary Results Expected Outcomes Timeline Implications Summary Question and Answers

## Slide 38: Summary
Can we design and analyze adaptive navigation methods for multirobot systems to maneuver through complex and dynamic vector fields to specified regions and trajectories interest?
This research will extend the work of multirobot in vector fields by:
  Creating a methodological way of modelling vector fields for multirobot research.
  Creating a catalogue of regions of interest within vector fields.
  Design and Analysis of control primitives for vector fields.
  Demonstrate success off these primitives in simulation and on a physical test bed.
Findings can be implemented in existing controller architectures.
Findings are applicable on land, sea, sky, and space.

## Slide 39: Thank you
Question and Answers

## Slide 40: Appendix
References
Additional Slides

## Slide 41: References
[1] Adamek, Thomas, Christopher A. Kitts, and Ignacio Mas. "Gradient-based cluster space navigation for autonomous surface vessels." IEEE/ASME Transactions on Mechatronics20.2 (2014): 506-518.
[2] C. A. Kitts and I. Mas, "Cluster Space Specification and Control of Mobile Multirobot Systems," in IEEE/ASME Transactions on Mechatronics, vol. 14, no. 2, pp. 207-218, April 2009, doi: 10.1109/TMECH.2009.2013943.
[3] I. Mas, S. Li, J. Acain, and C. A. Kitts, “Entrapment/escorting and patrolling missions in multi-robot cluster space control,” in Proc. IEEE/RSJ Int. Conf. Intell. Robots Syst., St. Louis, MO, USA, Oct. 2009, pp. 5855– 5861.
[4] M. Woolsey, C. A. Kitts and M. A. Neumann, "Gradient-based Adaptive Navigation of Multiple Diving Autonomous Surface Vehicles," OCEANS 2022, Hampton Roads, Hampton Roads, VA, USA, 2022, pp. 1-8, doi: 10.1109/OCEANS47191.2022.9977006.
[5] C. A. Kitts and M. Egerstedt, “Design, control, and applications of real world multirobot systems [from the Guest Editors],” IEEE Robot. Autom. Mag., vol. 15, no. 1, p. 8, Mar. 2008.
[6] Lee, Robert K., et al. "3-d adaptive navigation: Multirobot formation control for seeking and tracking of a moving source." 2020 IEEE Aerospace Conference. IEEE, 2020.
[7] S. T. Hart and C. A. Kitts, "Unifying Control Architecture for Reactive Particle Swarms," in IEEE/ASME Transactions on Mechatronics, vol. 28, no. 2, pp. 873-883, April 2023, doi: 10.1109/TMECH.2022.3211155.
[8] Hart, Shae T., Jake Kamenetsky, and Christopher A. Kitts. "Dynamic Elliptical Shaping Control for Swarm Robots." IEEE Access 11 (2023): 17454-17470
[9] McDonald, Robert T., et al. "Navigation of scalar fronts with multirobot clusters in simulation and experiment." IEEE Systems Journal 14.3 (2020): 3755-3766.
[10] C. A. Kitts, R. T. McDonald, and M. A. Neumann, “Adaptive navigation control primitives for multirobot clusters: Extrema finding, contour following, ridge/trench following, and saddle point station keeping,” IEEE Access, vol. 6, pp. 17 625–17 642, 2018.
[11] Trakas, Panagiotis S., Andreas Tantoulas, and Charalampos P. Bechlioulis. "Formation Control of Nonlinear Multi-Agent Systems with Nested Input Saturation." Applied Sciences 14.1 (2023): 213.
[12] Matveev, Alexey, et al. "Non-Gradient Based Tracking of Environmental Field Isolines in a Changing Medium by Dubins-Vehicle Type Robots." IEEE Transactions on Automatic Control (2023).
[13] Cooper, Ryan, et al. "Initial Study of Multirobot Adaptive Navigation for Exploring Environmental Vector Fields." 2019 IEEE Aerospace Conference. IEEE, 2019.
[14] Mas, Ignacio, and Christopher Kitts. "Quaternions and dual quaternions: Singularity-free multirobot formation control." Journal of Intelligent & Robotic Systems 87 (2017): 643-660.
[15] Wang, J., Guo, Y., Fahad, M., and Bingham, B., 2019, “Dynamic Plume Tracking by Cooperative Robots,” IEEE/ASME Transactions on Mechatronics, early access.
[16] Braquet, Martin, and Efstathios Bakolas. "Vector field-based collision avoidance for moving obstacles with time-varying elliptical shape." IFAC-PapersOnLine 55.37 (2022): 587-592.

## Slide 42: References
[17] Liddy, Tommie, et al. "Obstacle avoidance using complex vector fields." Proc. of the 2008 Australasian Conference on Robotics and Automation, Canberra, Australia. 2008.
[18] Nelson, Derek R., et al. "Vector field path following for miniature air vehicles." IEEE Transactions on Robotics 23.3 (2007): 519-529.
[19] Hu, Bin-Bin, et al. "Spontaneous-Ordering Platoon Control for Multirobot Path Navigation Using Guiding Vector Fields." IEEE Transactions on Robotics (2023).
[20] Garg, Kunal, and Dimitra Panagou. "Finite-time estimation and control for multi-aircraft systems under wind and dynamic obstacles." Journal of Guidance, Control, and Dynamics 42.7 (2019): 1489-1505.
[21] Yao, Weijia, et al. "Singularity-free guiding vector field for robot navigation." IEEE Transactions on Robotics 37.4 (2021): 1206-1221.
[22] Rajabhandharaks, Danop, et al. "Indoor Testbed for Vector Field Multirobot Adaptive Navigation: Feasibility Study." International Design Engineering Technical Conferences and Computers and Information in Engineering Conference. Vol. 59292. American Society of Mecha nical Engineers, 2019.
[23] Matveev, Alexey, et al. "Gradient-free tracking of unsteady environmental level sets in dynamic environments by a nonholonomic robot." IFAC-PapersOnLine 53.2 (2020): 9256-9261.
[24] R. K. Lee, C. A. Kitts, M. A. Neumann and R. T. Mcdonald, "Multiple UAV Adaptive Navigation for Three-Dimensional Scalar Fields," in IEEE Access, vol. 9, pp. 122626-122654, 2021, doi: 10.1109/ACCESS.2021.3107854.
[25] Thangavelautham, Jekan, and Yinan Xu. "Co-Evolution of Multi-Robot Controllers and Task Cues for Off-World Open Pit Mining." arXiv preprint arXiv:2009.09149 (2020).
[26] Kalita, Himangshu, et al. "Guidance, navigation and control of multirobot systems in cooperative cliff climbing." arXiv preprint arXiv:1701.07553 (2017).
[27] Bychkov, I. V., A. A. Tolstikhin, and S. A. Ulyanov. "A lobster-inspired multi-robot control strategy for monitoring non-stationary concentration fields." Journal of Physics: Conference Series. Vol. 2099. No. 1. IOP Publishing, 2021.
[28] Li, Shuai, Ruofan Kong, and Yi Guo. "Cooperative distributed source seeking by multiple robots: Algorithms and experiments." IEEE/ASME Transactions on mechatronics 19.6 (2014): 1810-1820..
[29] Gonçalves, Vinicius Mariano, Ryan McLaughlin, and Guilherme AS Pereira. "Precise landing of autonomous aerial vehicles using vector fields." IEEE Robotics and Automation Letters 5.3 (2020): 4337-4344.
[30] Woolsey, Max, Michael A. Neumann, and Christopher A. Kitts. "Spiral Search Pattern for Scalable Assemblages of Uncrewed Surface Vehicles." OCEANS 2023-MTS/IEEE US Gulf Coast. IEEE, 2023.
[31] Hoy, Michael, Alexey S. Matveev, and Andrey V. Savkin. "Algorithms for collision-free navigation of mobile robots in complex cluttered environments: a survey." Robotica 33.3 (2015): 463-497.
[32] Ogren, Petter, Edward Fiorelli, and Naomi Ehrich Leonard. "Cooperative control of mobile sensor networks: Adaptive gradient climbing in a distributed environment." IEEE Transactions on Automatic control 49.8 (2004): 1292-1302
[33] Bhatia, Harsh, et al. "The Helmholtz-Hodge decomposition—a survey." IEEE Transactions on visualization and computer graphics 19.8 (2012): 1386-1404.

## Slide 43: AN Primitive - Intersecting Vectors Technique